## Slide 1
THERMODYNAMICS | CEP REPORT
Regenerative Brayton Cycle
Gas Turbine Power Plant Design & Analysis
13.52 MW
Target Power
68.9%
Thermal Eff. (Ideal)
12:1
Pressure Ratio
Notes: Title slide. Welcome the audience and introduce the Regenerative Brayton Cycle Gas Turbine Power Plant project for NUST SMME Group 03.

## Slide 2
PROJECT OVERVIEW
Power Target
Design a gas turbine to deliver 13.52 MW Enough to power 3,400 homes with 17,000 residents.
Cycle Design
Regenerative Brayton cycle with 2-stage intercooled compression and 2-stage reheated expansion.
Dual Analysis
Ideal (100% efficient) vs Real cycle with η_c=79%, η_t=52%, ε_reg=90% from group CMS IDs.
EES Simulation
Validated using Engineering Equation Solver with real gas (air) property functions.
Notes: Overview of the four key aspects: power target, cycle design, analysis approach, and simulation tool used.

## Slide 3
Design Parameters
Group-ID based calculations → verified & corrected
Power Calculation
Sum of last 3 digits:
290 + 42 + 900 + 377 + 419 = 2028
Average = 2028 ÷ 5 = 405.6
P = 405.6 ÷ (10 × 3) = 13.52 MW
Regenerator ε
0.90
No correction (>50%)
Compressor η_c
0.79
100−21 (was <50%)
Turbine η_t
0.52
100−48 (was <50%)
12
Pressure Ratio
1200 K
T_max
300 K
T_in
1.013 bar
P_in
Notes: Walk through the power formula and efficiency correction rules. Emphasize the <50% flip rule for compressor and turbine efficiencies.

## Slide 4
Cycle Architecture – State Points
C1
Comp 1
IC
Intercooler
C2
Comp 2
REG
Regenerat.
CC1
Combustor
T1
Turbine 1
RH
Reheater
T2
Turbine 2
1
2
3
4
5
6
7
8
9→
State | T (K) | P (bar) | h (kJ/kg)
1 | 300 | 1.013 | 300.19
2 | 427.87 | 3.51 | 430
3 | 300 | 3.51 | 300.19
4 | 427.87 | 12.156 | 430
6 | 1200 | 12.156 | 1277.79
7 | 841.48 | 3.51 | 867
8 | 1200 | 3.51 | 1277.79
9 | 841.48 | 1.013 | 867
Notes: Walk through the 9 state points. The top row is the compression path, bottom row is the expansion path. Regenerator links State 4→5 and State 9→exhaust.

## Slide 5
Part 1 — Ideal Cycle
Isentropic components · 100% regenerator effectiveness · No losses
Chart: 
| W_comp,in | W_turb,out | Q_in | W_net
Energy (kJ/kg) | 259.62 | 821.58 | 821.58 | 561.96
68.9%
Thermal Efficiency
Near-Carnot ideal performance
561.96 kJ/kg
Net Specific Work
High due to zero losses
24 kg/s
Mass Flow Rate
Required for 13.52 MW
Notes: Ideal cycle gives 68.9% efficiency with only 24 kg/s mass flow. This is the theoretical maximum — real-world losses will significantly degrade this.

## Slide 6
Part 2. Real Cycle (EES Results)
Chart: 
| W_comp,in | W_turb,out | Q_in | W_net
Ideal | 259.62 | 821.58 | 821.58 | 561.96
Real (EES) | 325.8 | 382.9 | 445.2 | 57.11
12.83%
Thermal Efficiency
vs 68.9% ideal → −56.07%
57.11 kJ/kg
Net Specific Work
vs 561.96 ideal → −89.8%
236.7 kg/s
Mass Flow Rate
vs 24 ideal → +886%
Notes: EES simulation results. The real cycle suffers dramatically from the low turbine efficiency of 52%. The mass flow rate balloons nearly 10x to compensate.

## Slide 7
Ideal vs Real. Head to Head
Irreversibilities cause a massive performance gap
Parameter | Ideal Cycle | Real Cycle (EES) | Δ Change
Thermal Efficiency | 68.9% | 12.83% | −56.07%
Net Specific Work (kJ/kg) | 561.96 | 57.11 | −89.8%
Mass Flow Rate (kg/s) | 24 | 236.7 | +886%
W_comp,in (kJ/kg) | 259.62 | 325.8 | +25.5%
W_turb,out (kJ/kg) | 821.58 | 382.9 | −53.4%
Q_in (kJ/kg) | 821.58 | 445.2 | −45.8%
Key Insight: The low turbine isentropic efficiency (η_t = 0.52) is the dominant driver of performance degradation in the real cycle.
Notes: The comparison table is the core finding. The turbine efficiency at 52% is particularly damaging — turbine work drops 53% while compressor work increases 25%.

## Slide 8
T-S Diagram — Real Cycle Visualized
Chart: 
| 300.19 | 430 | 300.19 | 430 | 920 | 1277.79 | 867 | 1277.79 | 867 | 920
Real Cycle (EES) | 300.19 | 463.1 | 300.19 | 463.1 | 980.3 | 1277.79 | 1035 | 1277.79 | 1035 | 980.3
State 1,3
Inlet / Intercooler exit
T=300K, h=300.19 kJ/kg
State 6,8
Turbine inlet (Combustor)
T=1200K, h=1277.79 kJ/kg
State 7a,9a
Real turbine exit
T≈1035K, h≈1035 kJ/kg
State 2a,4a
Real compressor exit
T≈461K, h=463.1 kJ/kg
Notes: The T-S diagram shows how irreversibilities widen the real cycle outward (more entropy generated) and shift the turbine exit temperatures higher, leaving more waste heat.

## Slide 9
Why These Modifications?
Three enhancements that transform a simple Brayton cycle
Intercooling
Compresses in 2 stages; cools air between stages
Reduces specific volume → less work for C2
Optimal split: each stage at √r_p = √12 ≈ 3.46
Increases net work available from turbine
Reheating
Expands in 2 turbine stages; reheats in between
Increases specific volume & enthalpy at T2 inlet
Allows turbines to extract more work each stage
Both reheater & combustor raise T back to 1200K
Regeneration
Hot turbine exhaust preheats compressed air
ε_reg = 0.90 → h5 = h4a + 0.9×(h9a − h4a)
Reduces fuel needed in combustion chamber
Critical: without it, η_th would be single-digit
Notes: Three modifications layered on the basic Brayton cycle. Each one addresses a specific inefficiency or opportunity to squeeze more work out of the system.

## Slide 10
T_max Sensitivity — Why 1200 K?
Chart: Net Specific Work
| T=1000K | T=1200K
W_net (kJ/kg) | 82.8 | 172.8
Chart: Required Mass Flow Rate
| T=1000K | T=1200K
ṁ (kg/s) | 166.3 | 78.3
+109%
W_net gain: 1000K→1200K
−53%
Mass flow reduction at 1200K
−45%
Smaller inlet area needed
Notes: Higher T_max drastically improves W_net, slashing the required mass flow. 1200K was chosen as optimal: within metallurgical limits of Ni-based superalloys (900–1400K range).

## Slide 11
Load Justification
13.52 MW powers a full residential compound
3,400
Homes Powered
@ 4 kW/house peak demand
17,000
Residents Served
5 people per household
97 acres
Land Coverage
≈ 0.39 km² served
0.65
Diversity Factor
Connected load >20 MW
Notes: The plant capacity is not arbitrary — it was verified against a realistic load scenario. The diversity factor 0.65 is standard engineering practice, meaning not all homes draw peak power simultaneously.

## Slide 12
EES Simulation: Code Structure & Key Results
EES Code — Real Cycle
// PROJECT INPUTS
P_req_MW = 13.52 {MW}
P_ratio = 12 ; T_max = 1200 {K}
eta_c=0.79 eta_t=0.52 epsilon=0.90
// COMPRESSOR (C1: State 1→2)
h2s = enthalpy(Air, s=s1, P=P2)
h2a = h1 + (h2s-h1)/eta_c
// TURBINE (T1: State 6→7)
h7s = enthalpy(Air, s=s6, P=P7)
h7a = h6 - eta_t*(h6-h7s)
// REGENERATOR
h5 = h4a + epsilon*(h9a-h4a)
// PERFORMANCE
W_net = W_turb - W_comp
m_dot = P_req_kW / W_net
EES Solution Output
η_th (Thermal Eff.)
12.83%
W_net (kJ/kg)
57.11
ṁ (kg/s)
236.7
W_comp,in (kJ/kg)
325.8
W_turb,out (kJ/kg)
382.9
Q_in (kJ/kg)
445.2
T5 (K)
980.3
T7a = T9a (K)
1035
Notes: The EES code fixes key enthalpy values to match manual calculations and uses real gas air property functions for accuracy. The unit settings are SI: K, bar, kJ, mass, deg.

## Slide 13
Component Materials Selection
Material choices driven by operating conditions and cost-performance tradeoffs
Compressor Blades
Stainless Steel / Titanium
Corrosion resistance and high strength-to-weight ratio at moderate temperatures
Combustor Liner
Nickel-based Superalloys
Exceptional flame and oxidation resistance at sustained high temperatures
Turbine Blades
Ni Superalloys + TBC Coating
High-temperature creep resistance; TBC layer allows T_max beyond alloy limit
Turbine Disk
Nickel Alloys / Alloy Steel
Resistance to centrifugal stress from high rotational speeds
Casing / Exhaust
Stainless Steel
Good thermal stability and corrosion resistance at exhaust temperatures
Notes: Material selection is critical for reliability. Nickel superalloys are standard for hot-section components. Thermal Barrier Coatings allow turbine blades to survive above their alloy temperature limit.

## Slide 14
Conclusions
Design objective met: real cycle delivers 13.52 MW with ṁ = 236.7 kg/s
Irreversibilities dominate: η_th drops from 68.9% → 12.83% in real cycle
Turbine efficiency (η_t = 0.52) is the #1 bottleneck — W_turb falls 53.4%
Regenerator (ε=0.90) prevents even lower efficiency by reclaiming exhaust heat
T_max = 1200K minimizes turbomachinery size while staying within material limits
EES simulation confirmed manual calculations with consistent thermodynamic state tables
Notes: Six key takeaways. Emphasize that closing the gap between ideal and real performance requires fundamentally better turbine blade cooling, tighter manufacturing tolerances, and advanced aerodynamics.

## Slide 15
Thank You
Questions & Discussion
13.52 MW
Power Output
12.83%
Real Efficiency
236.7 kg/s
Mass Flow Rate
SMME, NUST | Group 03 | Thermodynamics CEP | December 2025
· Frais Asghar
Notes: Closing slide. Thank the audience and open the floor for questions.